## Slide 1: Development of a Simulation Model for Analysis and Evaluation of Human-Machine Collaboration in Assembly Cells
Author: João Pedro Caldas Ferreira @ FEUP Supervisor: António Almeida @ INESC-TEC
Search.…

## Slide 2: Table of Contents
Search.…
Introduction
Overview of the research context and objectives.
1
State of the Art
Quick review of key technologies analyzed for the dissertation project.
2
Development
Explanation of key settings of the development of the simulation framework, along with its limitations.
3
Case Study
Presentation of the Bosch assembly line that was studied to evaluate the simulation framework.
4
Results
Discussion of results from the case study and comparison across different scenarios.
5
Conclusions
Critical analysis of findings, and suggestions for future research.
6

## Slide 3: 1 – Introduction
Context and Motivation
Search.…
The dissertation project was developed within Bosch Security Systems, located in Ovar, which is composed of multiple assembly lines, with different degrees of automation.
Development Environment
Industrial assembly lines are increasingly relying on the distribution of tasks between robots and human operators. The challenge is to create a framework that supports setup decision-making and enhances efficiency and flexibility by enabling digital integration testing of collaborative robots in assembly lines.
Motivacional Background

## Slide 4: 1 – Introduction
Objetives
Search.…
Study processes, sequences, patterns of operations, and task distribution.
1. Mapping
Development of the simulation framework based on the previous study.
2. Framework
Create a digital model of a specific assembly line.
3. Model
Validate the model by comparing it’s outputs to real-world data
4. Validation
Simulate differente improvement scenarios.
5. Simulation
Make a cost-benefit analysis of selected configuration
6. Analysis

## Slide 5: 1 – Introduction
Research Methodology
Search.…
A comprehensive database is used to identify and collect relevant scientific literature.
Reference manager to organize, annotate, and cite the selected articles efficiently.
AI-powered tool for summarizing, extracting insights, and querying uploaded articles.

## Slide 6: 2 – State of the Art
Industry 4.0
Search.…
Interoperability
Decentralization
Real-Time Capability
Modularity
Virtualization
Virtual scenario testing
Local decision-making
Real-time process tracking
Flexible task allocation
Framework integration
J. Lettori et al. DOI: 10.3233/ATDE220671 Wojciech Lewicki et al. DOI: 10.3390/app14166957

## Slide 7: 2 – State of the Art
Human-Robot Collaboration
Search.…
Why does it matter?
Combines human flexibility + robot precision
Improves efficiency and system adaptability
Reduces heavy and repetitive payloads for operators
Collaboration Types
Independent: Separate tasks
Sequential: Same product, different tasks
Simultaneous: Same product, same time
Supportive: Human + robot assist

## Slide 8: 2 – State of the Art
Digital Twins
Search.…

## Slide 9: 2 – State of the Art
Process Modeling
Search.…
Continuous
Discrete
Agent-Based
I can: Stay, Jump or Swim

## Slide 10: 2 – State of the Art
Simulation Tools
Search.…
Tool | License | Flexibility | Ease of Use | Visualization | Real-Time | Documentation
 | Open | High | Moderate | Moderate | Moderate | Extensive
 | Open | High | High | Limited | Limited | Extensive
 | Paid | Moderate | High | Advanced | High | Comprehensive
 | Paid | Moderate | High | Advanced | High | Comprehensive

## Slide 11: 2 – State of the Art
Driven Decision Support
Search.…
Benefits
Enhances scenario evaluation and supports iterative learning to strengthen operational planning.
Hybrid Production
Supports human-robot collaboration, resource allocation, and bottleneck identification.
Definition
Combines data, models, and user interaction to enhance decision-making.
Purpose
Enables “what-if” analyses of production scenarios without affecting real operations

## Slide 12: 3 – Development
Design Principles and Tool Justification
Search.…
Logic
Interface
The primary objective of the proposed framework is to provide a flexible, configurable, and realistic simulation environment to support scenario analysis and decision-making.
What are the goals?
SimPy was chosen because it is an open-source Python library that offers a flexible and precise engine for modeling processes.
Qt complements this by providing tools for creating an intuitive graphical interface, which makes the framework interactive and accessible.
Why SimPy and Qt ?

## Slide 13
Search.…
3 – Development
Architecture

## Slide 14: 3 – Development
Logic with SimPy – Process-Based Modeling
Search.…
To be done

## Slide 15: 3 – Development
Logic with SimPy – Simulation Entities
Search.…
Operator
(simpy.Resource)
Source
(simpy.Resource)
Process
(simpy.Resource)
Buffer
(simpy.Container)
Converyor
(simpy.Container)
Target
(simpy.Resource)

## Slide 16: 3 – Development
Logic with SimPy – Simulation Flow
Search.…
node.request()
env.timeout(process)
node.release()
node = next_node()
if needed: operator.request()
env.timeout(transport)
if not needed: operator.release()

## Slide 17: 3 – Development
Logic with SimPy – Errors and Failures Simulation
Search.…
Event Logging
Every event from piece movement and operator interaction is logged
Failures & Maintenance
MTBF – avg. time between failures
MTTR – avg. repair time
MTBM – avg. time between maintenance
TSLM – time since last maintenance
MTM – avg. maintenance duration
Piece Conformity Errors
Each process has a configurable defect rate
Detected defective parts are immediately rejected
Simulation Behavior
Non-conformities occur probabilistically
Failures and maintenance trigger at the respective threshold.
Preventive Maintenance

## Slide 18: 3 – Development
GUI with Qt – Main Window
Search.…
Simulation Framework Main Window

## Slide 19: 3 – Development
GUI with Qt – Adding Elements
Search.…
Add/Edit Element with Import Data Window

## Slide 20: 3 – Development
GUI with Qt – Model Validation
Search.…
Error Detected
Valid System
Validation Return Options

## Slide 21: 3 – Development
GUI with Qt – Simulation Parameters
Search.…
Simulation Parameters

## Slide 22: 3 – Development
Output Metrics - Flows
Search.…
Simulation Piece Flow Spreadsheet
Operator Workflow Spreadsheet

## Slide 23: 3 – Development
Output Metrics – KPIs and Efficacy
Search.…
Production KPIs Dashboard
Process Efficacy Spreadsheet

## Slide 24: 3 – Development
Framework Limitations
Search.…
Digital Twins and AI
The framework does not include automatic balancing, intelligent routing, or optimization features.
Simulation of CoBots
Cobot behavior was modeled based on field observations and internal assumptions.
Operator Behavior
Real operators level of experience and skill level are not modeled.
Operator simulation is linear and deterministic.
Physical World Modeling
The framework lacks physical aspects such as safety procedures or ergonomic factors.

## Slide 25: 4 – Case Study
Context
Search.…
Avenar Fire Detector
Bosch Security Systems, S.A., located in Ovar, operates a significant manufacturing facility that produces security and fire detection systems. The shop floor features multiple assembly lines dedicated to assembling complex products.
Industrial Context
L05B – Produces the Avenar fire detector in a three-operator regime, which relies almost entirely on human work.
L05C – Is a more automated version of L05B
Lines under Study
Same product, two different profiles → clear comparison study for manual vs automated HRC lines.
Why these two lines?

## Slide 26: 4 – Case Study
Modeling Methods
Search.…
i) Conceptual Models
Process flow diagrams
Built from on-site observations and engineer feedback
Excel timing mapped to tasks
ii) Digital Models
Modular discrete-event blocks per station
Normal distributions for time simulation
Blocks connect following the real flow
Operator Modeling
Operator as a resource with availability and cost
Task embedded in process blocks
Each operator task is a linked process

## Slide 27: 4 – Case Study
Assembly Line L05C - Diagram
Search.…
Block Diagram of L05C

## Slide 28: 4 – Case Study
Assembly Line L05C – Processing Times
Search.…
# | Process | Average Time (s)
1 | Stick the label | 3.73
2 | Fit the PCB in the jig | 4.04
3 | Assemble Components | 19.70
4 | Fit Jig Top + Supply Welding Robot | 4.23
5 | WeldComponents | 13.875
6 | RemoveJig + Place in the Buffer | 4.81
7 | Place in the Sensitivity Test + Scan Barcode | 2.64
8 | Sensitivity Test | 10.54
9 | Place in the Welder + Weld Components | 4.305
10 | Place in the Standby Test + Scan Barcode | 1.57
11 | Execute Standby Test | 8.335
12 | Rotate Switches | 2.19
13 | Finish Encasing + Place in Buffer | 3.505
14 | Stick Color Ring + Place in the Final Test | 2.27
15 | Execute Final Test | 16
16 | Individual Box + Color Ring + Scan + Dust Cover + Place in Collective | 11.97
Texto de suporte
L05C Bosch Provided Data

## Slide 29: 4 – Case Study
Assembly Line L05C – Simulation Model
Search.…
* Wrong image in the dissertation document
Simulation Model of L05C

## Slide 30: 4 – Case Study
Assembly Line L05B - Diagram
Search.…
Block Diagram of L05B

## Slide 31: 4 – Case Study
Assembly Line L05B – Processing Times
Search.…
# | Process | Average Time (s)
1 | Stick the label | 3.73
2 | Fit the PCB in the jig | 4.36
3 | Manual Component Assembly | 24.70
4 | Fit Jig Top + Supply Welding Robot | 4.23
5 | WeldComponents | 13.88
6 | RemoveJig + Place in the Buffer | 5.54
7 | Place in the Sensitivity Test + Scan Barcode | 2.45
8 | Sensitivity Test | 10.54
9 | Place in the Welder + Weld Components | 4.56
10 | Place in the Standby Test + Scan Barcode | 1.72
11 | Execute Standby Test | 8.42
12 | Rotate Switches | 2.14
13 | Finish Encasing + Place in Buffer | 3.505
14 | Place product in Final Test | 2.56
15 | Execute Final Test | 24
16 | Assemble Individual Box + Color Ring Check + Scan + Place | 11.97
17 | Close Individual Box + Stick Label + Place | 5.96
Texto de suporte
L05B Bosch Provided Data

## Slide 32: 4 – Case Study
Assembly Line L05B – Simulation Model
Search.…
Simulation Model of L05B

## Slide 33: 4 – Case Study
Simulation Setup
Search.…
Each scenario was executed for 25 simulated hours to match Bosch’s minimum baseline window for KPI extraction.
The economics were parameterized using PPC (Bosch’s unit profit per assembled unit) to translate throughput into revenue and estimate ROI and payback across scenarios.
This setup ensures that technical KPIs are directly comparable with other scenarios.
Simulation Setup Window

## Slide 34: 5 – Results
Evaluation Metrics
Search.…
Value-Added Time
The execution of added value operations in each given node.
Overall Cycle Time ()
Represents the average time interval between the completion of two consecutive pieces.
Throughput
Total number of average finished products per hour in a given simulation.
Processing Time
Total time each piece spends being processed, in each process.

## Slide 35: 5 – Results
L05C Case Study Results – Utilization per Station
Search.…
Station | Time (s) | % Utilization
PCB | 22.73 | 7.75%
Stick a Label L05C | 22.72 | 7.75%
Assemble Components Machine L05C | 22.67 | 7.73%
Assemble Machine Input Conveyor L05C | 18.56 | 6.33%
Assemble Machine Output Buffer L05C | 109.77 | 37.43%
Assemble Machine Output Conveyor L05C | 21.24 | 7.24%
Soldering L05C | 18.64 | 6.36%
Middle Buffer L05C | 2.57 | 0.87%
Sensitivity Test L05C | 10.52 | 3.59%
Manual Weld L05C | 5.80 | 1.98%
Standby Test L05C | 8.34 | 2.84%
Rotate Switches L05C | 2.35 | 0.80%
Encasing L05C | 3.44 | 1.17%
Workstation Buffer L05C | 6.44 | 2.19%
Final Test L05C | 16.11 | 5.49%
Final Test Input Conveyor L05C | 1.37 | 0.47%
Texto de suporte
Utilization per Station L05C

## Slide 36
L05C Case Study Results – Added Time Value
Search.…
Station | Manual (s) | Automatic (s) | Loading (s) | % of Total Time
Stick a Label L05C | 3.65 | 0.00 | 3.96 | 6.7%
Assemble Components Machine L05C | 0.00 | 19.70 | 0.00 | 17.3%
Assemble Machine Output Buffer L05C | 0.00 | 0.00 | 4.16 | 3.7%
Soldering L05C | 0.00 | 13.84 | 4.76 | 16.3%
Middle Buffer L05C | 0.00 | 0.00 | 2.54 | 2.2%
Sensitivity Test L05C | 0.00 | 10.44 | 0.00 | 9.2%
Manual Weld L05C | 4.24 | 0.00 | 1.55 | 5.1%
Standby Test L05C | 0.00 | 8.25 | 0.00 | 7.2%
Rotate Switchs L05C | 2.34 | 0.00 | 0.00 | 2.1%
Encasing L05C | 3.45 | 0.00 | 0.00 | 3.0%
Workstation Buffer L05C | 0.00 | 0.00 | 2.24 | 2.0%
Final Test L05C | 0.00 | 15.95 | 0.00 | 14.0%
Color Ring Check + Packing + Place on Collective L05C | 12.66 | 0.00 | 0.00 | 11.1%
* Wrong figure in this section of the dissertation document
Added Time Value per Station on L05C
5 – Results

## Slide 37
L05C Case Study Results – Comparison with Real Data
Search.…
Metric | Shift 1 | Shift 2 | Shift 3 | Average | Simulation
Throughtput (pcs/hr) | 146.44 | 152.51 | 152.11 | 150.30 | 158.48
(s) | 24.61 | 23.62 | 23.68 | 23.97 | 22.72
Metric | Shift 1 | Shift 2 | Shift 3 | Average | Simulation
Throughtput (pcs/hr) | 146.44 | 152.51 | 152.11 | 150.30 | 158.48
 | 24.61 | 23.62 | 23.68 | 23.97 | 22.72
Simulation aligns closely with reality, with a deviation of ~5.4%. The gap is expected since human behavior isn’t modeled, yet the model captures L05C’s dynamics and is valid for scenario testing and optimization
Side-by-side comparison between simulated L05C results and Bosch real data across three 25-hour shifts, using Throughput and as validation KPIs.
5 – Results

## Slide 38: 5 – Results
L05B Case Study Results – Utilization per Station
Search.…
Station | Avg Time (s) | % Utilization
PCB | 34.79 | 1.16%
Stick a Label L05B | 13.12 | 0.44%
Manual Component Assembly L05B | 30.70 | 1.02%
Workstation Space L05B | 68.04 | 1.02%
Soldering L05B | 31.56 | 1.05%
Middle Buffer L05B | 1970.46 | 65.70%
Sensivity Test L05B | 27.15 | 0.91%
Manual Weld L05B | 31.71 | 1.06%
StandbyTest L05B | 29.21 | 0.97%
Rotate Switch L05B | 31.46 | 1.05%
Encasing L05B | 31.90 | 1.06%
Workstation Buffer L05B | 678.34 | 22.62%
Final Test Individual L05B | 20.95 | 0.70%
Texto de suporte
Utilization per Station L05B

## Slide 39: 5 – Results
L05B Case Study Results – Added Time Value
Search.…
Added Time Value per Station on L05B
Station | Manual (s) | Automatic (s) | Loading (s) | % of Total Time
Stick a Label L05B | 0.00 | 3.76 | 3.95 | 6.60%
Manual Component Assembly L05B | 21.59 | 0.00 | 0.00 | 18.30%
Workstation Space L05B | 0.00 | 0.00 | 3.15 | 2.70%
Soldering L05B | 0.00 | 13.80 | 5.45 | 16.30%
Middle Buffer L05B | 0.00 | 0.00 | 2.44 | 2.00%
Sensivity Test L05B | 0.00 | 10.46 | 0.00 | 8.50%
Manual Weld L05B | 3.76 | 0.00 | 1.55 | 4.30%
Standby Test L05B | 0.00 | 8.25 | 0.00 | 6.70%
Rotate Switch L05B | 2.14 | 0.00 | 0.00 | 1.70%
Encasing L05B | 0.00 | 3.95 | 0.00 | 3.20%
Workstation Buffer L05B | 0.00 | 0.00 | 2.74 | 2.20%
Final Test Individual | 0.00 | 20.95 | 0.00 | 16.90%
Assemble Individual Box + Color Ring Check + Scan + Place | 7.05 | 0.00 | 5.85 | 10.40%

## Slide 40: 5 – Results
L05B Case Study Results – Comparison with Real Data
Search.…
Metric | Shift 1 | Shift 2 | Shift 3 | Average | Simulation
Throughtput (pcs/hr) | 92.94 | 96.14 | 95.76 | 94.95 | 103.56
(s) | 35.32 | 34.77 | 35.37 | 35.15 | 34.76
Metric | Shift 1 | Shift 2 | Shift 3 | Average | Simulation
Throughtput (pcs/hr) | 92.94 | 96.14 | 95.76 | 94.95 | 103.56
 | 35.32 | 34.77 | 35.37 | 35.15 | 34.76
The simulation aligns closely with reality, with a deviation of only 9%. Because individual human behaviors are not modeled, and the flow assumes uninterrupted operation, slight output overestimation is expected.
Side-by-side comparison between simulated L05B results and Bosch real data across three 25-hour shifts, using Throughput and as validation KPIs.

## Slide 41: 5 – Results
Solution for L05B – Integration Description
Search.…
Consolidates Sensitivity Test + Resistor Welding + Stanby Test into one coordinated loop.
A cobot manages the testing, loads components into an autonomous welder, transfers them to the standby test, and outputs to a slide buffer.
Operates within an isolated acrylic or glass enclosure, with the operator feeding into an input buffer and receiving from the slide buffer.
Loading time of N(2.43 s, 0.41 s).
Processing time of N(17.42 s, 0.80 s).
L05B Bosch Model
L05B Solution Model

## Slide 42: 5 – Results
Solution for L05B – Implementation Cost
Search.…
Estimating that the integration would require 5 working days, and assuming an effective daily workload of 7.70 hours.
Given an average production of 94.95 pieces an hour and a PPC of 8.6€, the temporary suspension would cost about 31,438€.
The final implementation would cost at a minimum of: 94,438 €
* Rough Estimates Based on Feedback from Bosch Industrial Engineers
Cost Component | Estimated Cost (€)
Cobot arm (including controller base software) | 30,000 – 50,000
Custom gripper / end effector | 5,000 – 10,000
Safety enclosuyre and physical isolation | 5,000 – 15,000
Integration, programming, and validation | 15,000 – 30,000
Layout adaptation and auxiliary rquipment | 5,000 – 10,000
Operator training and knowledge transfer | 3,000 – 7,000
Total Estimated Cost | 63,000 – 122,000

## Slide 43: 5 – Results
Solution for L05B – Implementation Results
Search.…
L05B | Real | Simulation | Solution
Throughtput (pcs/hr) | 94.95 | 103.56 | 123.40
(s) | 35.15 | 34.76 | 29.17
L05B | Real | Simulation | Solution
Throughtput (pcs/hr) | 94.95 | 103.56 | 123.40
 | 35.15 | 34.76 | 29.17
Side-by-side comparison between the real, the simulated and the solution L05B throughput and as validation KPIs.
The solution represents a 19% improvement in production throughput.
* % improvement value wrong in the disseration document

## Slide 44: 5 – Results
Solution for L05B – Process Time
Search.…
Station | Avg Time (s) | Utilization
PCB | 29.25 | 1.16%
Stick a Label L05B | 21.59 | 0.38%
Manual Component Assembly L05B | 21.59 | 1.08%
Workstation Space L05B | 3.30 | 0.16%
Soldering L05B | 15.82 | 0.79%
Middle Buffer L05B | 810.31 | 40.42%
Cobot Input Buffer L05BV2 | 29.19 | 1.46%
Cobot (Sensitibity + Weld + Standby) L05BV2 | 96.31 | 4.80%
Cobot Output Buffer L05BV2 | 268.51 | 13.40%
Rotate Switch L05B | 29.09 | 1.45%
Encasing L05B | 29.80 | 1.49%
Workstation Buffer L05B | 642.70 | 32.06%
Final Test Individual L05B | 20.95 | 1.05%
Texto de suporte
Utilization per Station on L05B Solution

## Slide 45: 5 – Results
Solution for L05B – Added Time Value
Search.…
Station | Manual (s) | Automatic (s) | Loading (s) | % of Total Time
Stick a Label L05B | 0.00 | 3.74 | 3.97 | 8.30%
Manual Component Assembly L05B | 21.59 | 0.00 | 0.00 | 23.10%
Workstation Space L05B | 0.00 | 0.00 | 3.15 | 3.40%
Soldering L05B | 0.00 | 13.80 | 1.95 | 16.80%
Middle Buffer L05B | 0.00 | 0.00 | 0.5 | 0.5%
Cobot (Sensitivity + Weld + Standby) | 0.00 | 12.33 | 0.00 | 11.30%
Rotate Switch L05B | 2.11 | 0.00 | 0.00 | 1.90%
Encasing L05B | 0.00 | 3.92 | 0.00 | 3.50%
Workstation Buffer L05B | 0.00 | 0.00 | 2.76 | 2.40%
Final Test Individual | 0.00 | 20.95 | 0.00 | 17.90%
Assemble Individual Box + Color Ring Check + Scan + Place | 7.07 | 0.00 | 5.83 | 11.00%
Added Time Value per Station on L05B Solution

## Slide 46: 5 – Results
Cost-Benefit Considerations
Search.…
Metric | Value
Baseline Daily Output | 797.41 pcs
Improved Daily Output | 950.18 pcs
Baseline Days to Produce 2589 pcs | 3.25 days
Improved Days to Produce 2589 pcs | 2.72 days
Time Saved | 0.52 days
Extra Pieces in Equal Time | 484 pcs
Extra Profit Generated | 4,163.53 €
Implementation Cost | 94,438 €
Estimated Payback Time | 73.26 days
Texto de suporte

## Slide 47: 6 – Conclusions
Critical Assessment
Search.…
Human Factors Exclusion
Ergonomics and fatigue are not considered leading to potential operator-centric design gaps.
Computational Efficiency
The DES kernel (Simpy) handles queuing, resource contention, and task preemption, however, high-load simulations have not been thoroughly tested.
Configurational Agility
Core abstractions let us reconfigure assembly lines fast, like adding a cobot and reassigning OP2 needed minimal changes.
Fidelity vs Practicality
The more accurate and realistic the data, the higher the fidelity of the simulation output will be.

## Slide 48: 6 – Conclusions
Alignment with Dissertation Objectives
Search.…
Map the main processes and operational routing in the Bosch Ovar assembly cells that could be automated using robotic systems.
Develop a simulation model using an appropriate platform (e.g., Arena, AnyLogic, FlexSim).
Simulate various operational scenarios and task-distribution strategies between operators and robots, taking into account production times and cadence, operating costs, and assembly cell flexibility.
Perform scenario analyses of operator–robot task allocation, including a sensitivity analysis based on different levels of operator experience and training.
Conduct a cost–benefit analysis of the proposed solution.
Propose improvements, optimizations, and best practices for the current production processes in Bosch assembly cells, based on the simulation results.

## Slide 49: 6 – Conclusions
Future Work
Search.…
Pathway to Digital Twin
Continuous development for real-time data integration and real-time visualization.
Results Automation
Future development should also prioritize the automation of result presentation dynamics to enhance the extraction of KPIs.
Broadened Resource Modeling
The framework can be expanded to support a wider range of industrial elements by incorporating machines, dynamic buffers, and more reliable cobots.
Use-Case Expansion
Strengthening the framework’s credibility requires broader deployment and testing.

## Slide 50: Development of a Simulation Model for Analysis and Evaluation of Human-Machine Collaboration in Assembly Cells
Author: João Pedro Caldas Ferreira @ FEUP – joao.p.caldas@inesctec.pt
Search.…
Thanks for the Attention